QF1056/QF1052/QF1055A phase-locked signal generator

| Specification | QF1056/B | QF1052/D | QF1055/A |
| --- | --- | --- | --- |
| Frequency Operate Freq. range Display Resolution CW Frequency error CW Frequency stability (after warm-up 30min) | 10Hz ~ 40MHz 6digit 100Hz ±(50×10-6+100Hz) ±(5×10-6+30Hz) / 15min | 0.3 ~ 170MHz 6digit 100Hz / 1KHz ±(50×10-6+100Hz) 0.3 ~ 30MHz ±(50×10-6+1KHz) 30 ~ 170MHz (5×10-6+30Hz) / 15min (50×10-6+30Hz) / 3h | 0.3 ~ 300MHz 6digit 1KHz ±(50×10-6+2KHz) ±(50×10-6+800Hz) /15min <40MHz ±(50×10-6+100Hz) /15min ≥400MHz |
| CW output Level range Level accuracy Attenuation range ATT. Error Output impedance V.S.W.R Hormones Residual AM% (r.m.s) Residual FM (r.m.s) RF leakage | -117 ~ +13dBm 10dB step 0.3μv ~ 1v ±1dB typical 0.6dB at +13dBm 50Ω 0 ~ 120dB ±1dB (0 ~ 80dB) ±2dB (90 ~ 120dB) 50Ω <-30dB (at+13dBm) ≤0.2% (BW50Hz ~ 15KHz) ≤50Hz (BW50Hz ~ 15KHz) ≤1μV | -19 ~ +112dBμ 1dBstep 0dBμ=1μV ±1dB 0 ~ 131dB ±1.5dB (0 ~ 112dB) ±2dB (113 ~ 131dB) 50Ω <1.6 (50Ω) ≤-30dBc (0.3 ~ 30MHz) ≤-45dBc (30 ~ 170MHz) ≤0.1% (BW20Hz ~ 15KHz) ≤30Hz (BW50Hz ~ 15KHz) ≤1μV | -126 ~ +3dBm 10dBstep 0.112mV ~ 316mV ±(±1dB±0.8dB)at+3dbm 50Ω 0~120dB ±1dB (0 ~ -60dB) ±1.5dB (-60 ~ -120dB) 50Ω ≤-25dB ≤0.5% fc≥40MHz ≤1% fc<40MHz <200Hz (BW50Hz ~15KHz) ≤1μV |
| AM% INT Modulation Modulation range AM accuracy AM distortion Residual FM (BW 50Hz~15KHz) EXT AM | 400Hz / 1KHz 0 ~ 90% 5%+F.S 5% <3% (Typical ≤2%) ≤300Hz at 1KHz AM<80% 30Hz ~ 10KHz <1Vrms AM30% | 400Hz / 1KHz 0 ~ 80% (0.1+3%) <30MHz (0.1+4%) >30MHz ≤1% ~ 1.5% AM<30% ≤3% ~ 3.5% AM<80% ≤300Hz at 1KH AM<80% 20Hz ~ 10KHz ≤2.5V r.m.s | 400Hz / 1KHz 0 ~ 80% (±5%+F.S 5%) <60% ±3% <10% <3% AM<60% ≤20×10-6 fc≥40MHz ≤20×10-6+300Hz fc≥40MHz 30Hz ~ 10KHz ≤1.5V r.m.s AM60% |
| FM Charateriation Max. Deviation INT-FM FM accuracy (at 1KHz) FM. Distortion (at 1KHz)BW 50Hz~15KHz Residual AM (at 1KHz BW50~15KHz) EXT FM Frequency Input voltage FM error | 0 ~ 100KHz in3range 400Hz / 1KHz ±5%+F.S ×5%,FM0 ~ 100KHz ±3% ~ 5% FM<30KHz ≤0.2% FM<100KHz <1% r.m.s 30Hz ~ 100KHz 1V r.m.s ±3dB | 0 ~ 99KHz 400Hz / 1KHz 12%+2KHz FM>10KHz 10%+1KHz FM>10KHz 0.25% FM<99KHz ≤0.5% fc<10MHz FM5KHz ≤0.5 fc>10MH FM50KHz 20Hz ~ 100KHz fc<30MHz <2.5V r,m,s ±3dB | 0 ~ 100KHz in 3 range 400Hz / 1KHz 5%+F.S 10% <0.8% FM 100KHz ≤1% fc<40MHz ≤3% fc<40MHz 30Hz ~ 100KHz <1.5V r.m.s ±3dB |
| EXT video Modulation (75Ω) Modulation Freq. Modulation responds | N / A | N / A | Only QF1055 AM 87.5% INPUT IV P-P 30Hz ~ 5.8MHz 1 ~ 12 Channel ±2dB |
| Power Dimension & width mm | <20W 220V ±10% 50Hz 300×426×132.5 8kg | 426×350×132.5 10kg | <20W 300×426×132.5 10kg |

# Text boxes

QF phase-locked signal generators series are RF standard signal generator, which use PLL Circuit ensure high accuracy and stability in the carrier generation.   FM/AM Modulation Signal or simultaneously can be applied to the carrier.  Accuracy output level cover very wide Range .  These advantage make QF generator is most suited for R / D department to measure receivers, amplifiers, filters and other circuit operating in the AM/FM and TV broadcast bands and quality assurance of communication and mobile radio Equipment .