QF4941 Radio Station Comprehensive Tester

QF4941 is the radio communication tester, it combines all required for AM/FM mobile transceiver (radio stations) testing to 965MHz with a single unit, such as:

RF signal synthesized generator,   RF Freq. Meter,   RF power meter,   Modulation meter (AM/FM), AF voltmeter,   AF distortion meter,   AF SINAD meter.  AF Freq. meter.

The light Weight , small size and compact make it particularly suitable for stationary and mobile use. QF4941 has excellent price/performance ratio.

QF4941 display with store for recall of panel tester all function can be entered directly via the key. It can meet both military demands and civil needs.

# Text boxes

Page 3-2

Page 3-1

- QF4941 combines all requirment for mobile communications, testing to 965MHz

- Particularly suitable for AM/FM mobile transceiver test.

■ Light weight, small size and compact.

- Large LCD Screen (Chinese Display).

- Excellent price/performance ratio

1.5 ~ 965MHz

0 ~ 25KHz

5%+1count (at 1KHz)          8.5%+1count (50Hz ~ 10KHz)

50Hz ~ 10KHz

<2%   (at 1KHz  FM: 5KHz       BW 0.3 ~ 3.4KHz)

15mV ~ 30W

<60Hz (<500MHz)             <80Hz(>500MHz)

(BW 0.3~3.4KHz and RF input >15mV)

50Hz ~ 15KHz                ±0.02%

0.1 ~ (50 ~ 800Hz) 1Hz (0.8 ~ 15KHz)

10mV ~ 3Vrms                ±5%+1mV    5Ω

<0.5% (at 1KHz)              <1% (50Hz ~ 15KHz)

20Hz ~ 20KHz  ±0.02%+1 count  (after warm-up 1 h.)

50mV ~ 30V

0.1Hz (<1KHz)  1Hz (>1KHz)

50Hz ~ 20KHz

0.1~30Vrms   ±3%+3mv+1count

1MΩ/ 40pf

BPF 0.3 ~ 3.4KHz   LPF300Hz    LPF50KHz

0.1 ~ 30Vr.m.s

0 ~ 30%  THP     ±5% ±0.5%

1KHz

1KHz

0.1 ~ 30Vr.m.s

10 ~ 45dB                   5%+0.5dB

400mVp-p

BPF   0.3 ~ 3.4KHz    LPF 300Hz    LPF 15KHz

10kΩ

Interface IEEE488              (GB / T15946-1995 standard)

SJ30374 standardⅡ

10 ~ 40℃ store T –40℃ ~ 70℃

360mm×280mm×166mm       25Kg

FM:

Range:

Deviation:

Accuracy:

Modulation Freq.:

Distortion:

Input level range:

Residual FM:

## AF signal generator:

Freq. Range:

Resolution:

AF output:

Distortion:

AF analysis:

AF Freq. Meter:

Measurement range:

Input level range:

Freq. resolution：

AF voltmeter meter:

Frequency range:

Volt range:

Impedance:

Filter :

Distortion meter:

Input range:

Distortion range:

Frequency:

SINAD meter :

Frequency. :

Input range:

Sinad range:

De-modulation output (real panel plot)

Output:

Post demodulation filter

Hmpedance:

EMC

Temperature：

Size & weight:

≤-106dBc / Hz  typical        (at 500MHz   offset 20KHz)

≤-100dBc / Hz                (at 965MHz   offset 20KHz)

≤60Hz                       (1~ 500MHz)

≤80Hz (500 ~ 965MHz)        (BW 0.3 ~ 3.4KHz)

≤0.5% (1 ~ 400MHz)           (BW 0.3 ~ 3.4KHz)

0 ~ 99% ±7%+1%            (at 1KHz        AM 0 ~ 80%)

±10%+1%                    (50Hz ~ 5KHz   AM 0 ~ 70%)

±15%+1%                    (50Hz ~ 15KHz  AM 0 ~ 85%)

<2.5%                        (at 1KHz        AM<30%  BW 0.3 ~ 3.4KHz)

50Hz ~ 15KHz

20Hz ~ 20KHz

0 ~ 25KHz

±7%+0.1KHz  (at 1KHz)        ±10%+0.1KHz   (100Hz ~ 15KHz)

≤±1%                        (at 1KHz   FM: 25KHz   BW: 0.3 ~ 3.4KHz)

50Hz ~ 15KHz

50Hz ~ 50KHz

1.5 ~ 965MHz

10Hz

1×10-6 +1 count               (after warm-up for 1 h.)

15mW ~ 30W

(1.5 ~ 965MHz)

5mW ~ 30W

0.1dB

±12%+1 count                  (<500MHz)

±15%+1 count                  (>500MHz)

1.5 ~ 400MHz

0 ~ 90%(MANUAL);  0 ~ 30% (AUTO):  (1.5 ~ 100MHz)

0 ~ 80% (MANUAL);  0 ~ 30% (AUTO):  (100 ~ 400MHz)

5%+1count (at 1KHz)             8%+1count (50Hz ~ 10KHz)

50Hz ~ 10KHz

<2% (21 ~ 40MHz)               <5% (1.5 ~ 21MHz)

(at 1KHz    AM30%    BW 0.3 ~ 3.4KHz)

15mV ~ 30W

<1%                             (BW 0.3 ~ 3.4KHz)

SSB phase noise:

Residual FM (CCITT  RMS):

Residual AM:

Modulation:

AM:

Range :

Error:

Distortion:

INT Modulation Freq.:

EXT Modulation Freq.:

FM:

Peak deviation:

Accuracy:

Distortion:

INT Modulation Freq.:

EXT Modulation Freq.:

## RF analysis

## RF Freq. Meter

Frequency:

Resolution:

Accuracy:

Input level:

RF power meter:

Power range:

Resolution:

Accuracy:

Modulation meter:

AM:

Range:

AM%:

AM%:

AM accuracy:

Modulation Freq. range:

Distortion:

input level range:

Residual AM:

1 ~ 965MHz.

1×10-6×carrier freq.±10Hz    (after warm-up)

50Hz    (<530MHz)          100Hz(530 ~ 965MHz)

≤15Hz / 15min (1~50MHz)     ≤0.5×10-6  / 15min (50 ~ 965MHz)

10MHz

≤1×10-6

0.2×10-8                                 after warm-up for 1 hour

≤±2×10-8 / day              after warm-up for 24 hours

-127~ -20dBm                50Ω

±2dB    (>-113dBm)        ±2.5dB(≤-113dBm)

0.1dB

≤1.8

≤3uV    (100 ~ 965MHz)     ≤5uV(1 ~ 300MHz)

<-25dBc  (1 ~ 395MHz)       ≤-20dBc(395 ~ 965MHz)

<-30dBc  (1 ~ 30MHz)         <-35dBc(30 ~ 90MHz)

<-40dBc  (90 ~ 965MHz)

RF synthesized signal generator.

### Frequency

Range:

Error.:

Resolution:

Stability:

### INT reference oscillator

Freq.:

Accuracy:

Stability:

Aging rate:

RF Output (dBm, uV, mV)

Range:

Error:

Resolution:

S.W.R:

RF leak leakage:

### Spectral purity

Sub-harmonics:

Non-harmonics:

#### Features

#### Overview

#### Main specifications