##### QF Series Synthesized Signal Generator

Qianfeng offers a wide selection of high-performance general purpose synthesized signal generator with versatile modulation capability.  Four modulation modes are offered: AM / FM / ΦM / PM (QF1480 only have two modes of AM and FM). These instruments are suitable for wide variety applications ranging from Broadcasting TV, communication to radar , navigation  and electron war etc .

These products are designed for manual as well as ATE applications and ideally suited for various test during product development.  They are also the great help for manufacturing of RF communication products such as cellular radio, or cordless phones. Excellent pulse modulation specification (rise/fall time < 15ns and 80 dB on/off ratio) is suited especially for electron war such as radar / electron against, etc.

Remote programming via the standard GPIB Bus.  They can store and recall for 50/100 complete front panel setting-up with internal non-volatile memory. built-in Microprocessor guarantees their advanced technical performance and use’s convenience.

| Model | QF1471 | QF1480 B / C | QF1481A |
| --- | --- | --- | --- |
| Frequency Range: Resolution: Accuracy: Switching speed: Internal ref. oscillator Aging rate: Accuracy | 3 ~ 520MHz 50Hz <±50×10-6 < 70ms 10MHz 10×10-6 / 15min. <±5×10-6 | 0.01 ~ 1050MHz 10Hz <±5×10-6 <70ms 10MHz <±5×10-7/mon. <±5×10-6 | 0.1 ~ 2100MHz 10 ~ 20Hz <±5×10-7 <70ms 10MHz <2×10-8 / day. <±5×10-7 |
| Output Range: Resolution Accuracy: R . P . P: S . W . R: Impedance: RF leakage: | -127 ~ +13dBm 0.1dB ±2.5dB yes 25W 25V ≤1.6:1 50Ω (N) <1uV | -127~ +13dBm 0.1dB ±1.5dB yes 50W 25V ≤1.5:1 50Ω (N) < 3uV | -137 ~ +13dBm (f> 1050MHz) -137 ~ +16dBm (f< 1049MHz) 0.1dB < 1.5dB f> 1MHz < 2dB f< 0.9999MHz yes 25W 25V ≤1.5:1 50Ω (N) < 3uV |
| Spectral purity Harmonics: Non-harmonics Sub-harmonics SSB phase noise Residual FM Residual AM | ≤-30dBc ≤-35dBc ≤55Hz ≤0.2% | ≤-30dBc < -60dBc < -122dBc/Hz < 12Hz BW 0.3～3KHz < -60dBc | ≤-30dBc (f>1MHz) <-60dBc (offset>10KHz) < -45dB < -122dBc / Hz < 6Hz (BW 0.3 ~ 3KHz) < -60dBc (BW 0.05~15KHz) |
| AM modulation Depth: Resolution: Accuracy: Distortion: Incidental FM INT modulation: fm EXT modulation: fm | 0 ~ 99% (≤ +7dBm) 0.1% (AM < 10%) 1% (AM > 10%) 8% (fm. 1KHz) ≤2% at 1KHz ≤300Hz 1KHz or 400Hz 20Hz ~ 20KHz | 0 ~ 99% (step 1%) 1% < 5% AM<90% <1.5% AM<30% 0.3fm 1KHz or 400Hz 20Hz ~ 30KHz | 0 ~ 99% (step 1%) 1% ±2%+4% of setting 1.5% AM<30% 0.3fm ~ 0.6fm 1KHz or 400Hz 20Hz ~ 50KHz |
| FM modulation Max. peak. deviation Resolution accuracy Distortion Incidental AM INT modulation(fm) EXT mode (fm) | 0~99KHz (FM>9.9KH) 1KHz (FM>9.9KHz ) 100Hz (FM<9.9KHz) 5%+2KHz ≤1% ≤1% 1KHz or 400Hz 50Hz ~ 110KHz | 100Hz ~ 99.9KHz 3 digits ±7% < 1% (FM> 100Hz) < 1% (at 1KHz rate) 1KHz or 400Hz 20Hz~30KHz | 0 ~ 400KHz 3 digits 7%+10Hz fm:0.3~20K < 1% <1% (at 1KHz rate) 1KHz or 400Hz 20Hz ~ 100KHz1 |
| ΦM modulation Phase deviation Resolution Accuracy Mod distortion | 0 ~ 25rad 0.1rad (< 10rad) 1rad (> 10rad) 8%+0.5rad <1% | N / A | 0 ~ 40rad 3LED 3 digits 7%+0.01rad (at 1KHz) 1% |
| Pulse modulation ON / OFF ratio Rise/fall time(10 ~ 90%) EXT mod repetition Rate INT mode | ≥ 50dB ≤ 30ns DC—10MHz TTL 1KHz or /400Hz | N / A | > 80dB < 15ns DC-16MHz 1KHz or /400Hz |
| Remote programming Interface Interface function | GPIB compatibility with IEEE-488 SH1,AH1,TS,TEO, L3,LEO,SR1,RL1,RP0,DC1,DT1,CO,E2 | IGPIB compatibility with IEEE-488 SH1,AH1,TS,TEO, L3,LEO,SR1,RL1,RP0,DC1,DT1,CO,E2 | GPIB compatibility with IEEE-488 SH1,AH1,TS,TEO, L3,LEO,SR1,RL1,RP0,DC1,DT1,CO,E2 |
| Other Store / recall EMI standard Power supply Operating temp. | 100 non-volatile register for store/recall meet with GB6833-9-87 GB6833-10-87 220V±10% 50Hz 0 ~ 40℃ | 50 non-volatile register for store/recall meet with GB6833-9-87 GB6833-10-87 220V±10% 50Hz 0 ~ 40℃ |
| Size weight | 450×426×132.5 13kg | 575×460×146 18kg | 575×460×146 18.3kg |

# Text boxes

### Overview

### Main specifications

#### QF1471

#### QF1480B/C

#### QF1481/A

Page 2-2

Page 2-1